## Slide 1: Data analysis and visualization (CS306) lab

## Slide 2: Lab 1
For all the experiments, you will need to submit a pdf file that should include
  all plots/images/figures
  the analysis as part of your answer to questions
  your code/script
All plots/figures should be labeled properly (x-axis, y-axis, title etc.)
You can use Matlab/Python for programming

## Slide 3: Lab 1
Objectives:
To study the effect of sampling in the domain of signal processing

## Slide 4: Lab 1: Exp1
Load signal_lab1.mat. The vector ‘signal1’ (assume this to be a continuous signal) is of length 1 second, and formed by a linear combination of two sinusoids of frequencies f1 and f2.
Determine f1, f2 and the Nyquist rate.
Sample the given signal uniformly at 3 different rates: (a) half the Nyquist rate, (b) at Nyquist rate, (c) 4 times Nyquist rate. In all the 3 cases, show a plot with sampled points overlaid on the original signal.

## Slide 5: Lab 1: Exp1 (contd.)
3. Continuing from previous part, reconstruct the original signal from the sampled versions using linear interpolation. In each of the 3 cases, compute the reconstruction error (mean squared error MSE). Hint: use interp1 command for interpolation
4. Which sampling rate results in highest error and why? Do you observe perfect reconstruction (error = 0) at Nyquist rate? if not what are the possible reasons?

## Slide 6: Lab 1: Exp2
Load signal_lab1.mat. The vector ‘signal2’ (assume this to be a continuous signal) is of length 1 second, and formed by a linear combination of three sinusoids of frequencies f1 f2, f3.
Determine f1, f2, f3 and the Nyquist rate. Show the frequency plots that you use.
Sample the given signal non uniformly at 2 different rates: (a) max(f1,f2,f3), (b) at Nyquist rate. To implement non-uniform sampling, use randomly generated points (at the 2 given rates). For each of the 2 cases, compute the reconstruction error (use linear interpolation), and compare it with the error obtained due to uniform sampling (at the 2 given rates). Does non-uniform sampling lead to lower reconstruction error? Can it lead to lower reconstruction error in any case?

## Slide 7: Lab 1: submission
Submit a single pdf file (per group) on Moodle
Deadline: 10/01/2017 (by 18:00)